## Slide 1
www.carteeh.org

## Slide 2: Lecture #19: Traffic-Related Air Pollution Exposure Assessment Methods
Misti Levy Zamora
Environmental Health & Engineering
Johns Hopkins School of Public Health
The author declares that there is no conflict of interest
Lecture Track(s): HT/TT
Notes:   Health Track (HT)—mainly targeted at urban planners, transportation planners, and engineers with limited knowledge of public health-related concepts;
  Transportation Track (TT)—mainly targeted at environmental epidemiologists and public health professionals with limited knowledge of transportation-related concepts; and;
  Planning and Policy Track (PPT)—mainly targeted at planners, civil servants, and policy and decision makers with particular interest in the science-policy link.

## Slide 3: Traffic-Related Air Pollutions (TRAP)
Vehicles emit thousands of diverse pollutants including carbon dioxide (CO2), carbon monoxide (CO), volatile organic carbons (VOCs), nitrogen oxides (NOx), particulate matter (PM), and benzene, formaldehyde, and lead (where leaded gasoline is used).
Vehicles can also produce pollutants through noncombustion processes such as resuspended road dust, tire wear, and brake wear.
Many of these individual pollutants can cause adverse effects on health and the environment.
The term “traffic-related air pollution” used in this presentation refers to exposure to primary emissions from vehicles (directly emitted), not the more broadly dispersed secondary pollutants that are derived from these emissions.
Notes: https://www.healtheffects.org/system/files/SR17TrafficReview_Exec_Summary.pdf
https://www.healtheffects.org/system/files/SR17TrafficReview.pdf
Traffic-related emissions contribute to both primary and secondary ambient pollutant concentrations against a background of similar contaminants emitted from stationary (point and area) sources.
Often, people choose to measure a group of VOCs, collectively known as BTEX, comprising benzene, toluene, ethylbenzene and xylene (often expressed as total xylenes (m+p). The BTEX suite has grown in popularity, as they are straightforward to monitor together, and provide a well-rounded picture of VOCs and are present in most urban areas.
Abrasion of surfaces and friction-induced mechanical disruption resuspends “road dust,” itself a complex mixture comprised predominantly of coarse particles (> 2.5 μm in aerodynamic diameter).8 Sandy, salty, dirty, and unpaved roadways can result in elevated concentrations of coarse particulate matter.9 The coarse fraction might contain earthcrustal material, along with asphalt, metals, latex tire fragments, pollens, and oil-coated particles. The wearing of vehicle parts, including tires and brake pads and discs, generates latex, metal, and ceramic debris.10 Motor oils evaporate off engine parts or drip onto road surfaces to become part of the complex mixture of contaminants. https://www.ncbi.nlm.nih.gov/pmc/articles/PMC2714822/

## Slide 4: What is an Exposure assessment?
The goal of human exposure assessment is to identify and quantify exposures to chemical, physical, and biological agents that may have adverse health effects.
Exposure assessment provides information on who is exposed and identifies the sources, routes and pathways for exposure in the real world at various life stages and provides data to understand and quantify health outcomes as they occur in various populations.
Exposure assessments are used to answer three primary questions:
  1. What are the characteristics of exposure (e.g., intensity, frequency, duration, route of entry)?
  2. How can the exposure be reduced?
  3. Has exposure changed over time?
Notes: Exposure assessments can be used to monitor status and trends in exposure over time. The emphasis for these assessments is on what the exposure is at a particular time and how it changes over time. This type of assessment is used to evaluate the potential for emerging health risks and impact of risk mitigation actions.

## Slide 5: Assessment Methods
Direct Measurements
Quantifying exposure based on traffic density instead of concentrations the pollutants themselves
Estimating TRAPS using proximity to roadways
Using an individual pollutant as a surrogate for all TRAP exposures
Using models to assess exposures for a group or individual
Using biological markers to assess internal dose of TRAPs
Using remote sensing to assess TRAP concentrations
Notes: https://www.sciencedirect.com/science/article/pii/S0160412005000905?via%3Dihub

## Slide 6: Direct Measurements
The actual measurement of motor-vehicle emissions is critically important for validating the emissions models.
A number of studies have measured pollution concentrations inside or immediately outside of vehicles traveling on roadways. This data can be extrapolated to a larger vehicle fleet.
Some studies also used data from the nearest regulatory monitoring stations in the study area to estimate traffic pollutant exposure.
A few studies have employed both personal and stationary monitors to provide better local estimates of exposure to traffic-related air pollutants.
Notes: (e.g., Gehring et al. 2006
Central air-pollutant monitoring stations, such as those established by the U.S. Environmental Protection Agency (U.S. EPA) for monitoring criteria pollutants, have been placed to measure population exposures on the urban or regional scales and have produced short- and long-term data on the temporal variability of selected air pollutants. Although the measurements at these stations are impacted by traffic-related pollutants, the stations are not able to capture local-scale perturbations caused by such pollutants.
https://www.healtheffects.org/system/files/SR17TrafficReview.pdf
Measurements of outdoor air quality on roadways indicate that concentrations of TRAPS are high compared with ambient concentrations measured at air-monitoring stations and are highly variable.

## Slide 7: Evaluation of Method
An advantage of regulatory data is that they are usually available on a daily basis and allow for time-series analyses.
However, the inability to account for small-scale spatial variability can lead to significant misclassification because central-site monitors are not designed to capture traffic variability.
Personal measurements are not always representative enough to extrapolate to a larger or different population
Factors influencing an individual’s personal exposure include activity patterns, meteorological conditions, land-use patterns, and socioeconomic status, which can be very unique.

## Slide 8: Exposure to Traffic Density
Instead of measuring the concentration of the pollutants themselves a number of studies have utilized direct measures of traffic to assess exposure levels
Traffic proxies include vehicle mix (i.e., diesel and gasoline-fueled vehicle volumes), traffic density or volume (for example, the daily number of vehicles), traffic density within buffers (from 50 to 5000 m), distance to roadways, street segments, and self-reported traffic exposures.
Several studies have determined the relationship between reported concentrations of individual air pollutants near roadways and traffic density and, in some cases, types and conditions of vehicles (cars, trucks, age of vehicles, etc.).
Notes: Lena et al. 2002; Janssen et al. 2001 Raaschou-Nielsen et al. 1997; Fischer et al. 2000; Adams et al. 2001b; Alili et al. 2001; Rijnders et al. 2001; Lena et al. 2002; Cape et al. 2004; Harrison et al. 2004b; Weijers et al. 2004; Fromme et al. 2005; Smargiassi et al. 2005; Westerdahl et al. 2005; da Silva et al. 2006)Chan et al. 1991; Ott et al. 1994; Lawryk et al. 1995; van Wijnen et al. 1995; Fromme et al. 1998; Rodes et al. 1998; Alm et al. 1999; Adams et al. 2001a; Chan and Liu 2001; Chan and Chung 2003; Lau and Chan 2003; Riediker et al. 2003; Behrentz et al. 2005; Kaur et al. 2005; Sabin et al. 2005; Westerdahl et al. 2005; Lewné et al. 2006; Saksena et al. 2006; Zhu et al. 2007; Fruin et al. 2008).
A few studies link traffic density to concentrations of surrogates near roadways or at homes. These studies have suggested that there is an association between variations in total traffic and composition of traffic (i.e., the mix of cars and trucks) and the concentrations of traffic-surrogate air pollutants near roadways. Each study, however, is most likely unique to the area it was conducted in and probably not easily transferable to other geographic areas, because the studies employed different measures of traffic density or vehicle volume; differed in traffic composition, specific vehicle conditions and characteristics; collected data at varying distances from roadways under varying meteorological conditions in different geographical areas; frequently did not account for background concentrations; and employed variable sampling periods and averaging times.

## Slide 9: Evaluation of Method
Assessing exposure of the population to traffic-related air pollution is complicated by several factors, including
  no single metric for traffic exposures
  traffic pollutants vary spatially
  other non-traffic sources contribute identical pollutants to ambient and indoor pollutants
Accurately measuring traffic exposure in both time and space is difficult (especially if was self-reported) and often impractical in large health studies.
The associations between pollutant concentrations and traffic density have been shown to vary with the pollutant measured and the features of the sampling sites.
Notes: Chan et al. 1991; Ott et al. 1994; Lawryk et al. 1995; van Wijnen et al. 1995; Fromme et al. 1998; Rodes et al. 1998; Alm et al. 1999; Adams et al. 2001a; Chan and Liu 2001; Chan and Chung 2003; Lau and Chan 2003; Riediker et al. 2003; Behrentz et al. 2005; Kaur et al. 2005; Sabin et al. 2005; Westerdahl et al. 2005; Lewné et al. 2006; Saksena et al. 2006; Zhu et al. 2007; Fruin et al. 2008

## Slide 10: Estimating Traffic-related air pollution using proximity to major roadways
TRAPs contribute to ambient air quality on a wide range of spatial scales, from local roadsides and urban scales to broadly regional background scales.
Many studies that have examined gradients in pollutants as a function of distance from busy roadways have indicated exposure zones for traffic-related air pollution in the range of 50 to 1500 m from highways and major roads, depending on the pollutant and the meteorological conditions.
Most pollutants return to background concentrations within 500 m.
The degree of gradient is a function of the reactivity of the specific pollutant
Meteorology plays an important role in determining the size and diurnal and seasonal stability of impact zones.
The exposure is then estimated at a residence based on the proximity to roadways
Notes: There have been hundreds of studies that examined factors affecting atmospheric concentrations of traffic-related air pollutants. The studies have varied greatly in pollutant measurement methods, sampling times, numbers of measurements, distances from traffic, traffic characteristics (such vehicle mix, vehicle use, and traffic volume), study location, microenvironments, sampling seasons, and meteorological conditions.
Studies that have sampled the exhaust of moving vehicles in real-world situations (specifically, in tunnels or on roadways) have contributed very useful information about the emissions rates of the current vehicle fleet and also have allowed the evaluation of the impact of new emission-control technologies and fuels on emissions.
proximity models (direct measures of traffic) are the easiest to implement, they are error prone because they ignore the parameters that affect the dispersion and physicochemical activity of the pollutants.

## Slide 11: Estimating Traffic-related air pollution using proximity to major roadways
Notes: https://www.healtheffects.org/publication/traffic-related-air-pollution-critical-review-literature-emissions-exposure-and-health
Downwind concentrations were elevated between 250 and 400 m from the roadway compared with upwind distances of 200 m.
Although the overall patterns of distance decay for most traffic pollutants were well correlated with those for NO2, there were major differences between the upwind and downwind transects.

## Slide 12: Evaluation of Method
The associations between pollutant concentrations and traffic density have been shown to vary with the pollutant measured and the features of the sampling sites.
Zhu and colleagues (2002) found that pollutant concentrations were systematically higher downwind than upwind and decreased with increasing logarithm of the distance from the highway

## Slide 13: Pollutant Surrogates for TRAP Exposures
A widely used approach to characterize traffic pollution is to utilize individual pollutants (also known as tracer compounds) as surrogates to represent exposures to all TRAPs.
The most commonly used traffic-pollutant surrogates include CO, NO2, elemental carbon (EC, or black carbon; BC), PM, benzene, and ultrafine particles (UFP). EC has been used as a surrogate for diesel exhaust.
A surrogate for traffic emissions should
  (1) have traffic as the dominant source of atmospheric emissions,
  (2) vary with other constituents of motor-vehicle exhaust over time,
  (3) be measurable at ambient concentrations using reasonably inexpensive and accurate methods
  (4) not have independent adverse health effects associated with it at concentrations encountered in various environments.
Notes: In addition, the ultimate goal in most epidemiologic studies is to relate individual exposures to some health-related out come, so a surrogate measure should reasonably approximate personal exposure to traffic emissions

## Slide 14: Evaluation of Method
None of the most commonly used traffic pollutants considered here as surrogates for traffic emissions (namely CO, NO2, PM mass and number, BC, and benzene) meet all of these criteria for an ideal surrogate for traffic related air pollution.
Little is known about the ratios of these surrogates to the complex pollutant mixtures emitted by traffic or how these ratios have varied over time or location.
In addition, little is known about the ratio of the surrogates to the secondary air pollutants associated with traffic
Notes: CO, benzene, and NOx (in this case NO2 ), found in on-road vehicle emissions, are components of emissions from all sources, making it difficult to disentangle the contributions from motor vehicles from other sources (including some in indoor environments)

## Slide 15: Exposure Models
A number of modeling techniques have been developed for estimating traffic-pollutant exposures that hold promise for use in large epidemiologic studies of traffic-related air pollution.
Traffic models that have been developed to predict local exposures to TRAPS include
  Proximity-based (most basic )
  Geostatistical interpolation
  Land-use-regression (LUR)
  Dispersion
  Hybrid individual-exposure models (combine time–activity data, personal measurements, and models)
They incorporate numerous parameters (such as meteorological variables, data on land use, traffic data, and monitoring data or emissions rates depending on the model) and can improve the spatial representation of the local impact of traffic against a background of regional and urban concentrations.
Notes: Assignment to Individual Address Once a predictive model for exposure is developed through the methods reviewed above, estimates are generally assigned to home addresses and occasionally to workplace or school locations
Following Jerrett and colleagues (2005a), this review divides the approaches into five major categories: (1) proximity-based models, (2) geostatistical interpolation, (3) LUR models, (4) dispersion models, and (5) hybrid models that combine one or more of the above four approaches with time−activity or personal monitoring data used to derive some measure of individual exposure (Jerrett et al. 2005a).
Geostatistical interpolation models are best implemented in conjunction with dense, well-distributed monitoring networks; their chief limitations are the size of the network and the number of measurements needed over time to estimate the spatial distribution of pollution surrogates accurately. Land-use regression is appealing in that it can account for the diversity of sources that contribute to a surrogate; however, the true contribution (in terms of associated variance) of traffic to the regression is not always known or reported. Dispersion models utilize motor-vehicle–emissions and air-quality data and incorporate meteorological data but must be calibrated correctly to realize their advantages. These models are very data- and computationintensive and depend on the validity of the model assumptions. Hybrid models that combine measurements of personal exposure to traffic surrogates or time–activity data with exposure models come closest to a logistically feasible “best” estimate of human exposure.
The most basic exposure-assessment methods are proximity-based models, in which indicators, or surrogates, of the relative concentrations of motor-vehicle-related pollutants are used to estimate an individual’s traffic exposure (see also section 3.II.3E). Proximity models assume that the distance to roadways (or traffic) from place of residence serves as a surrogate for exposure to traffic-related pollution. Although these models can be useful, they do not typically consider the compounded influence at residences that might be affected by numerous roadways with different traffic levels, nor do they account for potential meteorologic influences.
GEOSTATISTICAL INTERPOLATION MODELS - Interpolation models result in the creation of a pollution “surface,” an attribute that varies continuously over space within the study domain, in which pollution concentrations z at an unsampled location s0 are estimated at neighboring measured sites denoted as s1. Wong and colleagues (2004) identified four interpolation models for air-pollution exposure assessment: (1) spatial averaging, (2) nearest monitor, (3) inverse distance weighting, and (4) kriging. The most advanced form of spatial interpolation is kriging, which produces the best linear unbiased estimate and allows for mapping of error variances
LAND-USE REGRESSION MODELS LUR models treat the pollutant of interest as the dependent variable and proximate land-use, traffic, and physical environmental variables as independent predictors. They predict pollution concentrations at a given site based on surrounding land use and traffic characteristics. Validation of these models has shown that they generally perform as well as or better than dispersion models.
DISPERSION MODELS Air-quality dispersion models have been used for decades to estimate ambient concentrations from emission sources. Recently, Gaussian dispersion models have been used in conjunction with GIS. This combination has allowed information from empirical monitoring systems and data on population distribution in the study area to be analyzed together.
HYBRID INDIVIDUAL-EXPOSURE MODEL- The model relies on measured concentrations of pollutants in microenvironments (residential outdoor, residential indoor, school outdoor, school indoor, and in-vehicle), where children spend most of their time, to compute the timeweighted average exposure TXi for each child:
A number of modeling techniques have been developed for estimating traffic-pollutant exposures that hold promise for use in large epidemiologic studies of traffic-related air pollution.

## Slide 16: Evaluation of Method
Many areas have missing/outdated traffic data and undercount in light-traffic areas since the priority is high density areas
The accuracy of the inputs is critical to the usefulness of a given model
For some common pollutants, such as CO and NO, these cross-validations suggested good model performance in predicting ambient concentrations of traffic related pollutants
Once a predictive model for exposure has been developed estimates are generally assigned to home addresses (occasionally to workplace or school locations), but home address exposures may not be representative for the actual individual’s exposure

## Slide 17: Biological Markers
Biomarkers used in the epidemiology are usually divided into three categories: markers of internal dose, markers of early response, and markers of susceptibility.
Urinary metabolites of certain compounds may serve as biomarkers of exposure to traffic related pollutants.
1&2-amino-naphthalene and 1-hydroxy-pyrene can be used as a biomarker of exposure to TRAPS
Black carbon has been associated with decreases in exhaled breath condensate
Ozone and PM have been inconsistently associated with exhaled biomarkers.
High-resolution metabolomics is a sensitive tool for measuring environmental exposures and biological responses. This can be used to assess changes in both plasma and saliva samples.
Notes: Gong, Jicheng, Tong Zhu, Howard Kipen, David Q. Rich, Wei Huang, Wan-Ting Lin, Min Hu, and Junfeng Jim Zhang. "Urinary polycyclic aromatic hydrocarbon metabolites as biomarkers of exposure to traffic-emitted pollutants." Environment international 85 (2015): 104-110.
Patel, Molini M., Steven N. Chillrud, K. C. Deepti, James M. Ross, and Patrick L. Kinney. "Traffic-related air pollutants and exhaled markers of airway inflammation and oxidative stress in New York City adolescents." Environmental research 121 (2013): 71-78.
Liang, Donghai, Jennifer L. Moutinho, Rachel Golan, Tianwei Yu, Chandresh N. Ladva, Megan Niedzwiecki, Douglas I. Walker et al. "Use of high-resolution metabolomics for the identification of metabolic signals associated with traffic-related air pollution." Environment international 120 (2018): 145-154.

## Slide 18: Remote Sensing and TRAPS
Remote sensing has emerged as an important resource in the exposure sciences.
Remote sensing for studying exposures to in three categories:
(1) as a means of estimating the concentrations of certain pollutants
(2) as a direct data input to models used to predict air pollution from land use, traffic, or other ground-level information;
(3) as a means of cross-validation for land or atmospheric data captured by ground or traditional meteorological devices
Correlation coefficients of ground-based measurements and satellite data were greater than 0.4 in most locations and exceeded 0.8 in some locations.
Not all pollutants of interest can be measured remotely with adequate sensitivity.
Most satellites are too coarse to characterize the 500 m region from traffic
Notes: https://www.healtheffects.org/system/files/SR17TrafficReview.pdf
“Correlation coefficients between in situ measurements and estimates derived from Ozone Measuring Instrument (onboard the Aura satellite) of surface NO2 for the year 2005.”

## Slide 19: Research gaps and future directions
Characterizing TRAP exposures across age, gender, ethnic, and economic variables for residential location in the United States is needed.
More information on the composition and spatial variation of TRAP is needed for those components that have received less attention, such as metals.
The application of existing air-quality models to near-roadway issues has been somewhat limited by model uncertainty.
Studies linking traffic modification strategies to corresponding improvement in health effects or their associated biological markers are needed.
The relationship between exposure to near-roadway traffic emissions and health impacts have largely been based on residential location.
Notes: Since the epidemiology studies are based on past estimates of exposure from older vehicles, they may not provide an accurate guide to estimating health associations in the future.

## Slide 20: Take-Home Messages
Traffic leads to pollutant exposures for vehicle occupants, pedestrians, and residents of nearby homes, schools, and other buildings.
Traffic factors, such as age, type, fuels, roadway configurations, and geographical settings, impact exposures to the nearby populations.
The concentrations of emitted pollutants decrease as they are transported. Several key components of the complex mixture of traffic-derived pollutants have been found to follow a declining concentration gradient with distance from roadways.
There are several methods currently employed to assess exposures including: direct measurements, estimating exposures based on traffic density, estimating TRAP concentrations using proximity to roadways, using a surrogate, using exposure models, using biological markers, and using remote sensing tools.
All methods can provide valuable information about exposures; however, none of the methods are perfect representations for all exposures.

## Slide 21: List of Abbreviations
  1. Carbon Monoxide (CO)
  2. Sulfur Dioxide (SO2)
  3. Nitrogen Dioxide (NO2)
  4. Ozone (O3)
  5. PM10 (particulates < 10 µm diameter)
  6. PM2.5 (particulates < 2.5 µm diameter)
  7. Lead (Pb)
  8. US Environmental Protection Agency (EPA)
  9. Nitrogen oxides (NOx),
  10. Particulate matter (PM),
  Traffic-Related Air Pollutions (TRAP)
  Elemental carbon (EC)
  Black carbon BC)
  ultrafine particles (UFP)
  Land-use-regression (LUR)

## Slide 22: Relevant Definitions
Duration: the length of time of contact with a pollutant
Frequency: the number of exposure events in an exposure duration
Route of entry: the way a pollutant enters the body after contact (e.g., by ingestion, inhalation, dermal application)
Dose: amount of pollutant that enters the body
Biologically Effective Dose: the amount of a pollutant that actually reaches cells
Acute Exposures: short-term exposures to a pollutant which may or may not be repeated
Chronic Exposures: exposures that are present for long periods of time; possibly life-long; possibly constant
Direct assessment methods measure the contact of a person with the pollutant in the exposure medium over an identified period (e.g., Personal Sampling, Biological Markers)
Indirect assessment methods estimate exposures bases on estimates derived from environmental monitoring (i.e., measurements made in locations frequented by the study participants), models, or questionnaires.
Notes: The intake fraction of a pollutant is defined as the proportion of emissions of the pollutant inhaled by an individual or population and quantifies the “exposure efficiency” of an emission source (Bennett et al. 2002; Marshall et al. 2005).

## Slide 23: References
Alm S, Jantunen MJ, Vartiainen M. 1999. Urban commuter exposure to particle matter and carbon monoxide inside an automobile. J Expo Anal Environ Epidemiol 9:237–244.
Adams HS, Kenny LC, Nieuwenhuijsen MJ, Colvile RN, Gussman RA. 2001a. Design and validation of a high flow personal sampler for PM2.5. J Exposure Anal Environ Epidemiol 11:5–11.
Adams HS, Nieuwenhuijsen MJ, Colvile RN. 2001b. Determinants of fine particle (PM2.5) personal exposure levels in transport microenvironments, London, UK. Atmos Environ 35:4557–4566.
Alili F, Momas I, Callais F, Le Moullec Y, Sacre C, Chiron M, Flori JP. 2001. Exposure to traffic pollution: Comparison between measurements and a model. Arch Environ Health 56:552–558.
Behrentz E, Sabin LD, Winer AM, Fitz DR, Pankratz DV, Colome SD, Fruin SA. 2005. Relative importance of school bus-related microenvironments to children's pollutant exposure. J Air Waste Manage Assoc 55:1418–1430.
Bennett DH, Margni MD, McKone TE, Jolliet O. 2002. Intake fraction for multimedia pollutants: A tool for life cycle analysis and comparative risk assessment. Risk Anal 22:905–918.

## Slide 24: References
Cape JN, Tang YS, van Dijk N, Love L, Sutton MA, Palmer SCF. 2004. Concentrations of ammonia and nitrogen dioxide at roadside verges, and their contribution to nitrogen deposition. Environ Pollut 132:469–478.
Chan LY, Chan CY, Qin Y. 1999. The effect of commuting microenvironment on commuter exposures to vehicular emission in Hong Kong. Atmos Environ 33:1777–1787.
Chan LY, Liu YM. 2001. Carbon monoxide levels in popular passenger commuting modes traversing major commuting routes in Hong Kong. Atmos Environ 35:2637– 2646.
Chan CC, Ozkaynak H, Spengler JD, Sheldon L. 1991. Driver exposure to volatile organic compounds, CO, ozone and NO2 under different driving conditions. Environ Sci Technol 25:964–972.
Chan AT, Chung MW. 2003. Indoor-outdoor air quality relationships in vehicle: Effect of driving environment and ventilation modes. Atmos Environ 37:3795–3808.
Gehring U, Heinrich J, Krämer U, Grote V, Hochadel M, Sugiri D, Kraft M, Rauchfuss K, Eberwein HG, Weichmann HE. 2006. Long-term exposure to ambient air pollution and cardiopulmonary mortality in women. Epidemiology 17:545–551.
HEI Air Toxics Review Panel. 2007. Mobile-Source Air Toxics: A Critical Review of the Literature on Exposure and Health Effects. Special Report 16. Health Effects Institute, Boston, MA.
Health Effects Institute. Panel on the Health Effects of Traffic-Related Air Pollution, 2010. Traffic-related air pollution: a critical review of the literature on emissions, exposure, and health effects (No. 17). Health Effects Institute.

## Slide 25: References
Gong, Jicheng, Tong Zhu, Howard Kipen, David Q. Rich, Wei Huang, Wan-Ting Lin, Min Hu, and Junfeng Jim Zhang. "Urinary polycyclic aromatic hydrocarbon metabolites as biomarkers of exposure to traffic-emitted pollutants." Environment international 85 (2015): 104-110.
Fischer PH, Hoek G, van Reeuwijk H, Briggs DJ, Lebret E, van Wijnen JH, Kingham S, Elliott PE. 2000. Traffic-related differences in outdoor and indoor concentrations of particles and volatile organic compounds in Amsterdam. Atmos Environ 34:3713–3722.
Fromme H, Lahrz T, Hainsch A, Oddoy A, Piloty M, Rüden H. 2005. Elemental carbon and respirable particulate matter in the indoor air of apartments and nursery schools and ambient air in Berlin (Germany). Indoor Air 15:335–341.
Fromme H, Oddoy A, Piloty M, Krause M, Lahrz T. 1998. Polycyclic aromatic hydrocarbons (PAH) and diesel engine emission (elemental carbon) inside a car and a subway train. Sci Total Environ 217:165–173
Fruin S, Westerdahl D, Sax T, Sioutas C, Fine PM. 2008. Measurements and predictors of on-road ultrafine particle concentrations and associated pollutants in Los Angeles. Atmos Environ 42:207–219.
Harrison RM, Jones AM, Lawrence RG. 2004b. Major component composition of PM10 and PM2.5 from roadside and urban background sites. Atmos Environ 38:4531–4538.
Janssen NAH, van Vliet PHN, Aarts F, Harssema H, Brunekreef B. 2001. Assessment of exposure to traffic related air pollution of children attending schools near motorways. Atmos Environ 35:3875–3884.
Kaur S, Nieuwenhuijsen M, Colvile R. 2005. Personal exposure of street canyon intersection users to PM2.5, ultrafine particle counts and carbon monoxide in central London, UK. Atmos Environ 39:3629–3641

## Slide 26: References
Jerrett M, Arain A, Kanaroglou P, Beckerman B, Potoglou D, Sahsuvaroglu T, Morrison J, Giovis C. 2005a. A review and evaluation of intraurban air pollution exposure models. J Expo Anal Environ Epidemiol 15:185–204.
Liang, D., Moutinho, J.L., Golan, R., Yu, T., Ladva, C.N., Niedzwiecki, M., Walker, D.I., Sarnat, S.E., Chang, H.H., Greenwald, R. and Jones, D.P., 2018. Use of high-resolution metabolomics for the identification of metabolic signals associated with traffic-related air pollution. Environment international, 120, pp.145-154.
Lena TS, Ochieng V, Carter M, Holguín-Veras J, Kinney PL. 2002. Elemental carbon and PM2.5 levels in an urban community heavily impacted by truck traffic. Environ Health Perspect 110:1009–1015.
Lawryk NJ, Lioy PJ, Weisel CP. 1995. Exposure to volatile organic compounds in the passenger compartment of automobiles during periods of normal and malfunctioning operation. J Expo Anal Environ Epidemiol 5:511–531
Lau WL, Chan LY. 2003. Commuter exposure to aromatic VOCs in public transportation modes in Hong Kong. Sci Total Environ 308:143–155.
Lewné M, Nise G, Lind ML, Gustavsson P. 2006. Exposure to particles and nitrogen dioxide among taxi, bus and lorry drivers. Int Arch Occup Environ Health 79:220–226.
Marshall JD, Teoh S-K, Nazaroff WW. 2005. Intake fraction of nonreactive vehicle emissions in US urban areas. Atmos Environ 39:1363–1371.
Ott W, Switzer P, Willits N. 1994. Carbon-monoxide exposures inside an automobile traveling on an urban arterial highway. J Air Waste Manage Assoc 44:1010–1018.
Patel, Molini M., Steven N. Chillrud, K. C. Deepti, James M. Ross, and Patrick L. Kinney. "Traffic-related air pollutants and exhaled markers of airway inflammation and oxidative stress in New York City adolescents." Environmental research 121 (2013): 71-7

## Slide 27: References
Raaschou-Nielsen O, Skov H, Lohse C, Thomsen BL, Olsen JH. 1997. Front-door concentrations and personal exposures of Danish children to nitrogen dioxide. Environ Health Perspect 105:964–970.
Rijnders E, Janssen NAH, van Vliet PHN, Brunekreef B. 2001. Personal and outdoor nitrogen dioxide concentrations in relation to degree of urbanization and traffic density. Environ Health Perspect 109:411–417.
Riediker M, Williams R, Devlin R, Griggs T, Bromberg P. 2003. Exposure to particulate matter, volatile organic compounds, and other air pollutants inside patrol cars. Environ Sci Technol 37:2084–2093.
Rodes C, Sheldon L, Whitaker D, Clayton A, Fitzgerald K, Flanagan J, DiGenova F, Hering S, Frazier C. 1998. Measuring concentration of selected air pollutants inside California vehicles. Final report prepared for California Air Resources Board Contract No. 95–339.
Saksena S, Luong PV, Quan DD, Nhat PT, Tho DT, Quang TN, Dang PN, Nguyen T, Quynh LN, Duc DH, Flachsbart PG. 2006. Commuters' exposure to particulate matter and carbon monoxide in Hanoi, Vietnam: A pilot study. EastWest Center Working Papers, No. 64. East-West Center. Honolulu, HI.
Sabin LD, Behrentz E, Winer AM, Jeong S, Fitz DR, Pankratz DV, Colome SD, Fruin SA. 2005. Characterizing the range of children's air pollutant exposure during school bus commutes. J Expo Anal Environ Epidemiol 15:377–387.
Smargiassi A, Baldwin M, Pilger C, Dugandzic R, Brauer M. 2005. Small-scale spatial variability of particle concentrations and traffic levels in Montreal: A pilot study. Sci Total Environ 338:243–251.

## Slide 28: References
da Silva AS, Cardoso MR, Meliefste K, Brunekreef B. 2006. Use of passive diffusion sampling method for defining NO2 concentrations gradient in São Paulo, Brazil. Environ Health 5:19.
Weijers EP, Khlystov AY, Kos GPA, Erisman JW. 2004. Variability of particulate matter concentrations along roads and motorways determined by a moving measurement unit. Atmos Environ 38:2993–3002
Westerdahl D, Fruin S, Sax T, Fine PM, Sioutas C. 2005. Mobile platform measurements of ultrafine particles and associated pollutant concentrations on freeways and residential streets in Los Angeles. Atmos Environ 39:3597–3610.
White, R.H., Spengler, J.D., Dilwali, K.M., Barry, B.E. and Samet, J.M., 2005. Report of workshop on traffic, health, and infrastructure planning. Archives of environmental & occupational health, 60(2), pp.70-76.
van Wijnen JH, Verhoeff AP, Jans HW, van Bruggen M. 1995. The exposure of cyclists, car drivers and pedestrians to traffic related air-pollutants. Int Arch Occup Environ Health 67:187–193.
Zhou Y, Levy JI. 2007. Factors influencing the spatial extent of mobile source air pollution impacts: A meta-analysis. BMC Public Health 7:89
Zhu YF, Hinds WC, Kim S, Shen S, Sioutas C. 2002. Study of ultrafine particles near a major highway with heavyduty diesel traffic. Atmos Environ 36:4323–4335.

## Slide 29: Reading List
https://www.healtheffects.org/publication/traffic-related-air-pollution-critical-review-literature-emissions-exposure-and-health