## Slide 1
www.carteeh.org

## Slide 2: Lecture #5: Air Quality Monitoring and Use in Compliance Determination
Wen-Whai Li, Ph.D., P.E.
The University of Texas at El Paso
wli@utep.edu; (915) 747-8755
Materials used in the presentation are for education and discussion purposes only. Do not use or cite the materials without the permission of the author
The author declares that there is no conflict of interest
Lecture Track(s): HT/TT/PPT
Notes:   Health Track (HT)—mainly targeted at urban planners, transportation planners, and engineers with limited knowledge of public health-related concepts;
  Transportation Track (TT)—mainly targeted at environmental epidemiologists and public health professionals with limited knowledge of transportation-related concepts; and;
  Planning and Policy Track (PPT)—mainly targeted at planners, civil servants, and policy and decision makers with particular interest in the science-policy link.

## Slide 3: Introduction
Background for National Ambient Air Quality Standards
Air Pollution Control Strategies and Philosophies
Air Quality Monitoring Used in Compliance Determination
QA/QC of Air Quality Data
Instruments for Compliance Monitoring
Purposes for Non-compliance monitoring
Discussion and Summary
Notes: Air pollution control by regulations has been widely adopted globally. Industrialized countries were quick to recognize the urgency of taking actions against air pollution in the early 20th century. The United Kingdom began to regulate air emissions as early as in 1906 [4]. However, the U.S. has been the world leader in taking systemic regulatory actions against air pollution since 1955. Many countries have since developed their own air quality control acts by adopting or modifying some landmark U.S. regulations. As to this date, air quality regulations are well developed in many countries and may differ from one another. This section dose not attempt to discuss the difference, effectiveness, and/or appropriateness among the various air quality guidelines and standards created by different nations. Rather, we focus on the development of several milestone air quality legislations in the U.S. as an illustration of the evolution of many similar air quality standards in the world.
Air quality in the U.S. deteriorated dramatically in the first half of the 20th century due to significant population growth, accelerated industrial outputs, and increased consumption of fossil fuels. As a result, an Air Pollution Control Act was promulgated in 1955 which paved the way for a series of air pollution reform acts later. Prior to 1955, only a limited number of air ordinances were installed in various municipalities, primarily cities with high industrial activities. For instance, Chicago and Cincinnati first established smoke ordinances in 1881 and Philadelphia passed an ordinance limiting the amount of smoke in flues, chimneys, and open spaces in 1904 [5]. In 1947, California authorized the creation of Air Pollution Control Districts in every county of the state.
There have been several amendments made to The Air Pollution Control Act of 1955. The Clean Air Act of 1963 was the first federal legislation regarding air pollution control. It established a federal program within the U.S. Public Health Service and authorized research into techniques for monitoring and controlling air pollution. In 1967, the Air Quality Act of 1967 was passed to expand federal government’s activities in air pollution control. In accordance to this law, enforcement proceedings were initiated in areas subject to interstate air pollution transport. As part of these proceedings, the federal government for the first time conducted extensive ambient air monitoring studies and stationary source inspections [5]. In 1969, another amendment was made to the act. This amendment further expanded the research on low emissions, fuels, and automobiles [6].
Public awareness of the state of the environment intensified in the 60s and reached a new peak in the 70s when the nation went through a tumultuous era of anti-war, liberalism, civil and women’s rights, energy crisis, and environmental movements. The 1970 Clean Air Act was enacted and completely replaced the 1967 Air Quality Act. This new Act also created the U.S. Environmental Protection Agency (EPA), as advised by President Nixon’s Advisory Council on Executive Organization [7]. It identified six common air pollutants of concern, called criteria pollutants, and required the EPA to develop technology-based National Ambient Air Quality Standards (NAAQS) to protect public health and welfare. Table 2.1 lists the six criteria pollutants identified in 1970: sulfur oxide (as sulfur dioxide), particulate matter, carbon monoxide, photochemical oxidants, hydrocarbons, and nitrogen dioxide, and their respective primary and secondary National Ambient Air Quality Standards. The primary and secondary NAAQSs were designed, respectively, to provide adequate margin of safety to protect public health and public welfare (including visibility, animals, crops, vegetation, and structures).

## Slide 4: U.S. National Ambient Air Quality Standards
Notes: In brief, air pollution control regulations in the U.S. have continued to evolve with amendments, updates, and revisions since 1970, as new findings of air pollutants on human health became available and new development in control and monitoring technologies became applicable and feasible. For instance, ozone (O3) was designated to replace the total photochemical oxidants as one of the criteria pollutants in 1979 and an annual fourth highest daily maximum 8-hour O3 average of 0.08 ppmv was installed to replace the not-to-be-exceeded 1-hour standard of 0.12 ppmv in 1997. EPA routinely conducts scientific reviews through the Clean Air Scientific Advisory Committee and makes new recommendations for public comments prior to issuing the final rules. Slide 4 shows the evolution of the NAAQS for ozone whereas Table 2.3 shows the evolution of the NAAQS for PM, two criteria pollutants which have gained increased attention due to their ubiquity and severe adverse health effects
Particulate Matter
National Ambient Air Quality Standard for Particulate Matter (National Ambient Air Quality Standards for Particulate Matter and Ozone; Final Rules July 18, 1997, 40 CFR Part 50, Section II-H):
Twenty-four hour average PM2.5 is met when the three-year average of annual 98th percentiles of 24-hr PM2.5 concentrations at each population-oriented monitor within an area is less than or equal to 65 g/m3, with fractional parts of 0.5 or greater rounding up;
The annual PM2.5 standard is met when the three-year average of the annual arithmetic mean PM2.5 concentrations, from single or multiple community-oriented monitors is less than or equal to 15 g/m3, with fractional parts of 0.05 or greater rounding up;
The 24-hour average PM10 is met when the three-year average of annual 99th percentiles of 24-hr PM10 concentrations at each monitor within an area is less than or equal to 150 g/m3;
The annual PM10 standard is met when the three-year average of the annual arithmetic mean PM10 concentrations at each monitor within an area is less than or equal to 50 g/m3, with fractional parts of 0.5 or greater rounding up.
The first two standards for PM2.5 are new. The third standard for 24-hour average PM10 is revised to be based on the three-year average of annual 99th percentiles of 24-hr PM10 concentrations at each monitor within an area from “with no more than one expected exceedance per year”.
Along with a National Ambient Air Quality Standard, the measurement instruments, methods, data collection, quality assurance protocols, laboratory methods, laboratory QA/QC, data reporting, time line for compliance. Many times, the sampling results are not only used for compliance purposes but also for identifying sources, assessing health risks, evaluating effectiveness of control devices, and determining areas of impacts. Thus, it is important to understand what we actually collect from the samplers.
New Development in 2006
EPA revised the air quality standards for particle pollution in 2006. The 2006 standards tighten the 24-hour fine particle standard from the current level of 65 micrograms per cubic meter (µg/m3) to 35 µg/m3, and retain the current annual fine particle standard at 15 µg/m3. The Agency decided to retain the existing 24-hour PM10 standard of 150 µg/m3. The Agency revoked the annual PM10 standard, because available evidence does not suggest a link between long-term exposure to PM10 and health problems.
New Development in 2012
EPA revised the air quality standards for particle pollution again in 2012. The annual fine particle standard is now at 12 µg/m3.
Ideal PM size distribution with three modes in ambient air
Nucleation mode: varies from 0.005 to 0.1 m and peaks at ~ 0.08 m, accounting for the preponderance of particles by number. Nucleation particle lifetimes are usually less than 1 hour because they rapidly coagulate with larger particles or serve as nuclei for cloud or fog droplets.
Accumulation mode: extends from 0.1 to 2.5 m, which accounts for most of the aerosol (particle) surface areas. The majority of sulfuric acid, ammonium, bisulfate, ammonium sulfate, ammonium nitrate, organic carbon, and elemental carbon is found in this range.
Coarse mode (or sedimentation mode): It varies between 2.5 to 25 m and peaks at around 10m. The peak of the coarse mode may shift between 6 and 25 m depending on the common emission sources in the region.

## Slide 5: Objectives of Federal and State Compliance Monitoring
Enforce compliance with regulatory environmental laws
Support implementation of air quality goals or standards
Assess the extent of pollution
Provide air pollution data to the general public
Evaluate the effectiveness of emissions control strategies
Provide information on air quality trends
Provide data for the evaluation of air quality models
Support research in public health and environment
Respond to emergencies and natural disasters
Notes: U.S. EPA regulates air pollution emissions form mobile and stationary sources under the CAA.
Definition of stationary sources and mobile sources (https://www.epa.gov/enforcement/air-enforcement#stationary)
Definition of point, area, and mobile sources by CAA.

## Slide 6: Historical Development of U.S. Ozone Standards
Table 2.2 Historical development of NAAQS for ozone
Notes: In brief, air pollution control regulations in the U.S. have continued to evolve with amendments, updates, and revisions since 1970, as new findings of air pollutants on human health became available and new development in control and monitoring technologies became applicable and feasible. For instance, ozone (O3) was designated to replace the total photochemical oxidants as one of the criteria pollutants in 1979 and an annual fourth highest daily maximum 8-hour O3 average of 0.08 ppmv was installed to replace the not-to-be-exceeded 1-hour standard of 0.12 ppmv in 1997. EPA routinely conducts scientific reviews through the Clean Air Scientific Advisory Committee and makes new recommendations for public comments prior to issuing the final rules. The table shows the evolution of the NAAQS for ozone whereas the next slide shows the evolution of the NAAQS for PM, two criteria pollutants which have gained increased attention due to their ubiquity and severe adverse health effects.

## Slide 7: Historical Development of U.S. PM Standards
Table 2.2 Historical development of NAAQS for ozone
Notes: (see previous note)

## Slide 8: U.S. National Ambient Air Quality Standards
Air Pollution Control Philosophies
- Emission Standards
- Air Quality Standards
- Emission Taxes
- Cost-benefit Analysis
Desirable Quality fro Air Quality Standards
- Cost Effectiveness
- Simplicity
- Enforceability
- Flexibility
- Evolutionary Ability
Notes: Anthropogenic air pollution is a main concern of the modern society. Anthropogenic air pollution is generally more persistent and toxic, with profound effects. It could cause significant adverse health effects to human beings and irreversible damage to the environment. Anthropogenic air pollution can be easily observed as smokestack emissions from industrial facilities, trapped emissions in routinely occurring urban temperature inversion layers, and hazes in national parks. Anthropogenic air pollutants can be emitted directly from a source or formed indirectly among airborne substances in the atmosphere chemically through chemical and/or photochemical reactions or physically through nucleation, accumulation, agglomeration, phase change, or decomposition. Air pollutants emitted directly from a source are called primary pollutants whereas those formed indirectly in the atmosphere are called secondary pollutants. The sources of air pollution are also classified into three categories according to the nature of the emissions’ source. A “point source” refers to a source that emits from a stationary, identifiable location such as a smokestack or a leak point in a container vessel. A “mobile source” refers to sources that are powered by combustion engines and can move on-road or off-road. Any other source that cannot be classified as point source or mobile source is called an “area source”, which in general represents sources with multiple unidentifiable locations or groups of sources with small amounts and/or unsteady-state emissions. Fugitive emissions from industrial related operations, small businesses, household activities (heating, cooking, cleaning, gardening) that are difficult to quantify and locate fall into the category of area sources. In the United States, for regulatory compliance enforcement, those point sources which emit or have the potential to emit 10 tons per year or more of a hazardous air pollutant or 25 tons per year or more of a combination of hazardous air pollutants are called “major sources”, as defined in Section 112 of the 1997 Clean Air Act Amendments (CAAA). Likewise, an “area source" is defined as any stationary source that is not a major source, i.e., emitting less than 10 tons per year or more of a hazardous air pollutant or 25 tons per year or more of a combination of hazardous air pollutants.

## Slide 9: QA/QC Requirements for Compliance Monitoring
Detectability (Determination of the Limit of Detection)
The low range critical value that a method-specific procedure can reliably discerns
Precision (within 10%)
The reproducibility of measurements as determined by collocated sampling using the same methods or by propagation of individual measurement errors determined by replicate analysis, blank analysis, and performance tests
Completeness (>75%)
The percentage of valid data reported compared to the total number of samples that are scheduled to be collected during the sampling period.
Repeatability (QA/QC Samples)
Collocated samples for PM and NO2 were further analyzed with the Pearson correlation analysis to evaluate possible bias resulted from the field protocols or laboratory analytical processes
Notes: Precision
Precision represents the reproducibility of measurements as determined by collocated sampling using the same methods or by propagation of individual measurement errors determined by replicate analysis, blank analysis, and performance tests (Watson et al., 2001). Precision, sm, can thus be defined as deviations from the average response to the same measurable quantity as follows:
sm = [( (Cm-C)2 )/ (n-1)]1/2
The project goal for precision is 10%, expressed as the coefficient of variation (CV), for values that exceed ten times their lower quantifiable limits.
Accuracy
Accuracy is the correctness of data and refers to the degree of difference between a measured value and a known or “true” value. For soil measurements, there are no known true values. Sampler accuracy will be measured by performance checks and audits between the sample collectors.
Detectability
Detectability is the low range critical value that a method-specific procedure can reliably discern. Analytical procedures and sampling equipment impose specific constraints on the determination of minimum detection limits (MDLs). For silt content and soil moisture content measurements, MDLs are determined in the prescribed ASTM method.
Completeness
Completeness is the percentage of valid data reported compared to the total number of samples that are scheduled to be collected during the sampling period. For this project, the completeness objective for all species and measurements is 75%. Completeness will be determined using the following:
Completeness = 100-[(Dx – Dc)/Dc] x 100
With regard to discrete measurements, Dx is the number of samples that valid results are obtained and Dc is the number of samples that scheduled to be collected and analyzed.
Representativeness
Representativeness is the degree to which data accurately and precisely represents a characteristic of a population, parameter variations at a sampling point, a process condition, or an environment condition. Temporal data representativeness cannot be achieved due to the limited time period for sampling. However, it can be assessed by comparing comparable measurements at existing sites reported in the literature.
Comparability
Comparability reflects the extent to which measurements of the same observable agree among different methods. Comparability may vary by method and meteorological conditions. Comparability will be assessed by comparing some sampled results with overlapping measurements and by comparing results to those, if available, reported for the existing sites.

## Slide 10: QA/QC Requirements for Compliance Monitoring
Calibration
  Standards
    Primary
    Direct measurement of the volumes by physical dimension alone, accuracy, ±0.3%
    Intermediate
    Cannot be done by direct physical dimension, Direct measurement of the volumes by physical dimension alone, accuracy, ±1 - 2%
    Secondary
    Calibrated against primary or intermediate standards under known conditions, accuracy, ±5%
Notes: A primary standard is a standard based only on one’s knowledge of the only three fundamental units: Mass, Length, Time
A secondary standard is any measuring device that has been calibrated against a primary standard.

## Slide 11: Instrument Calibration
Calibration
  Examples of Standards
    Primary
    Spirometer, bubble meter
    Intermediate
    Root meter, Dry gas meter
    Secondary
    Rotameter, orifice meter, Venturi meter
Notes: See Text books in Fluid Mechanics

## Slide 12: Design of Ambient Air Monitoring
Pollutants to be Monitored
Monitoring Locations
Duration of Monitoring
Sampling Methods and Procedures
Sampling Frequency
Sampling Plan
Sampling Media
Notes: Sampling Technologies
PM exists in the air with various shapes and densities. No sampling instrument (or at least not developed) can provide stepwise sharp cut of passing 100 % of PM small than a specific size and excluding 100 % of PM large than that specified size. As a result, the PM samples we collected in the air always include various sizes of PM. The methods used in PM sampling include inlet size selection, filtration, impaction, virtual impaction, and other technologies based on particle aerodynamics that are applicable in air pollution control. In any cases, size selective inlets are commonly used in every sampling instrument.
Sharp size cut-off cannot be achieved. Therefore, the goal is to develop an inlet that can have as sharp size cut-off as possible.
Size Cut-off: an instrument’s size cut-off is defined by the 50 % cut-point (d50). d50 represents the aerodynamic diameter at which 50 % of the sampled particles penetrate an inlet. The effectiveness of the sharp cut-off is defined by the slope of the sample effectiveness (or the ratio of d16/d84). A slope of 1 indicates that 100 % of the particles with aerodynamic diameter less than the cut-off pass through the inlet to the filter, and 0 % of those larger than the cut-point are collected. Typical values of the slope vary between 1.3 and 2. Figure 4.1 of EPA 1997 shows typical characteristics of sampling effectiveness curve for inlets. Figure 4.2 shows a conceptual graph of PM size distribution collected on filters. It appears that coarse PM collected on the filters are likely to be attenuated from what actually exist in ambient air.
J.C. Chow. 1995. Measurement methods to determine compliance with ambient air quality standards for suspended particles. JA&WMA. 45:320-382.
U.S. EPA. 1997. Draft guideline on speciated particulate monitoring.
U.S. EPA. 1997. 40 CFR Part 50. National Ambient Air Quality Standards for Particulate Matter and Ozone; Final Rules July 18, 1997.

## Slide 13: Instrumentation for Compliance Air Monitoring
Criteria Pollutants
  Particulate Matter
  Gaseous Pollutants
  Ozone
  NO2
  Lead
  SO2
  CO
Non-criteria Pollutants
Notes: “There are a number of Federal Reference Method (FRM) and Federal Equivalent Method (FEM) systems used to monitor the six criteria air pollutants (Lead [Pb], Carbon Monoxide [CO], Sulfur Dioxide [SO2], Nitrogen Dioxide [NO2], Ozone [O3], Particulate Matter [PM]) to determine if an area is compliant with the National Ambient Air Quality Standards (NAAQS) for these air pollutants. EPA publishes the list of active FRMs and FEMs on a semi-annual basis, but the list is not a comprehensive one, and anyone wishing to find information for all of the FRMs and FEMs must consult a large number of resources, since the information is not located in a single document. This report is the first attempt to list all of the available FRMs and FEMs in a single document.” (EPA, https://cfpub.epa.gov/si/si_public_record_report.cfm?Lab=NERL&dirEntryId=321491#:~:text=There%20are%20a%20number%20of,is%20compliant%20with%20the%20National)
URLs/Downloads:
REFERENCE AND EQUIVALENT METHODS USED TO MEASURE NAAQS CRITERIA AIR POLLUTANTS - VOLUME I_JUNE_23_2016.PDF (PDF,NA pp, 5966.978 KB, about PDF)
https://cfpub.epa.gov/si/si_public_record_report.cfm?Lab=NERL&dirEntryId=321491#:~:text=There%20are%20a%20number%20of,is%20compliant%20with%20the%20National

## Slide 14: Discussion
Objectives of Compliance Monitoring
Consistency in Monitoring Procedures and Equipment
Uncertainties involved in Compliance Monitoring
Related Meteorological Monitoring
  Surface Meteorology
  Upper Air Meteorology
Notes: Uncertainties
Repeatibility: with one laboratory using standard reference materials.
Reproducibility: consistency between different labs using the same technique
Instrument difference: specs, calibration, methods, etc
Instrument electronic drifting
Human errors

## Slide 15: Research Gaps and Future Directions
Contemporary issues on monitoring of biological airborne pollutants such as corona virus, SARS, MERS at transportation facilities and vehicles
Development of high-quality portable air sensors for rapid deployment and compliance monitoring
Portable and personal monitoring for precise monitoring of personal exposures to transportation emissions
Notes: Proprietary, state-of-the-art materials to be developed/updated.

## Slide 16: Take-Home Messages
Air quality monitoring is an integrated component in air quality management and assessment of health effects
Much of the compliance determination for transportation professionals resides on emission inventory and quantifications of vehicle emissions
The evolving compliance determination regulation for transportation activities has started to the determination of ambient pollutant concentrations and potential health impacts resulting from transportation emissions
It is thus important to understand the technologies and applicabilities of related air sensors and limitations
Notes: https://www.apti-learn.net/lms/register/display_document.aspx?dID=278
Contemporary issues to be developed/updated later.

## Slide 17: References
Li, W-W, 2020. Chapter 2: Air pollution, air quality, vehicle emissions and environmental regulations, in Traffic-Related Air Pollution: Emissions, Human Exposures, and Health, edited by Khreis H. et al, Elsevier S&T Books.
De Nevers, Noel. 2017. Air Pollution Control Engineering, Waveland Press, Inc., ISBN 1-4786-2905-3.
U.S. EPA, 2009. Monitoring Compliance Test and Source Testing Observation, Air Pollution Training Institute Course #468, December 2009.
U.S. Environmental Protection Agency (U.S. EPA), 2018. History of air pollution, U.S. EPA Research, Durham, NC 27711. <https://www.epa.gov/air-research/history-air-pollution#then>.

## Slide 18: Reading List
Khreis H. et al, 2020. Traffic-Related Air Pollution: Emissions, Human Exposures, and Health, Elsevier S&T Books.
De Nevers, Noel, 2017. Air Pollution Control Engineering, Waveland Press, Inc., ISBN 1-4786-2905-3.
U.S. EPA, 2009. Monitoring Compliance Test and Source Testing Observation, Air Pollution Training Institute Course #468, December 2009.
U.S. EPA, National Ambient Air Quality Standards (40 CFR part 50)

## Slide 19: Acknowledgements
The author acknowledges substantial materials adapted from several published documents “ Air Pollution Control Engineering’” by De Nevers , Waveland Press, Inc., ISBN 1-4786-2905-3, and “Monitoring Compliance Test and Source Testing Observation” by Air Pollution Training Institute Course #468, as well as information on the U.S. EPA websites. The information provided in this presentation is designed sole for discussion only and should not be cited or reproduced for any other uses.